## Slide 1
On rotary platform
HARP
Standard Configuration – raw signal through rotary joint
Required signal transmission
USB camera
2x optical sensor (7 lines, 5(?) signal, 2 power, ) OR 2x USB mouse
2x lick port
2x reward delivery
1x GND
Separate commutator for ephys (can be above or below stage)
Harp configuration
Optical sensor integration x2 (optional with USB mouse)
Lick port signal
Reward signal output
Rotary joint requirements
19 signal / power lines, 1 USB – OR (flow sensor)
  +12V, +5V, GND
5 signal / power lines, 3 USB (gaming mouse)
  +12V, +5V, GND
Through hole for air
Pros
Minimal electrical components on board rotary platform
Least additional testing / development required
Simple signal transmission
Existing off-the-shelf rotary joints with through-hole available
Power on board rotary platform not required
Cons
A lot of separate lines being passed through rotary joint (though check how many lines can be shared between flow sensors, e.g. CLK)
Concerns about reliability of USB signal transmission
Might require new rotary joint to scale up signal transmission
Concerns about I2C protocol being reliably read through rotary joint (for optical flow sensor), issue with long wires.
Concern about power stability over rotary joint, regulator on platform side?
Hall effect sensor
Incremental encoder
Notes: N.b. don’t necessarily need separate power lines for e.g. 24 vs. 12 vs 5, could pass 24 and regulate to different voltages
2 extra sensors to factor in, hall effect sensor, incremental encoder on the motor

## Slide 2
On rotary platform
HARP (Slave)
Standard Configuration – signal processed on board harp device
Required signal transmission
USB camera
2x optical sensor (7 lines) OR 2x USB mouse
2x lick port
2x reward delivery
1x GND
Separate commutator for ephys (can be above or below stage)
Synchronisation signal between two harp boards
Harp configuration
Optical sensor integration x2 (optional with USB mouse)
Lick port signal
Reward signal output
Rotary joint requirements
2 USB, through hole
Optional 4 power lines e.g. for valve power
Pros
Also minimal additional testing / development
Readily available rotary joint with through-hole
Simplification of signals leaving platform via rotary joint
Easy to scale up signals leaving platform since integrated on board harp, limited only by USB bandwidth
Cons
Extra electrical component on rotary platform, close to ephys, extra weight
Cannot power valves through harp USB. Solution could be to use hybrid joint with 4 power lines, or use battery pack for valve power
Concerns about reliability of USB transmission via rotary joint
Would need a separate device outside rotary platform to integrate incremental encoder and hall effect sensors
HARP signals must leave platform via USB, can’t interface directly with motor driver (without hybrid rotary joint)
Incremental encoder cannot be on rotary platform, so at least 1 USB signal must pass through rotary joint
Hall effect sensor
Incremental encoder
HARP (Master)
Notes: If we use the optical flow sensors vs. USB mouse, we need to use this solution (due to I2C / SPI communication problem through rotary joint).
Motor controller will have to be outside rotary platform so we may end up with 2 harp boards, one on platform, one off platform.
Slave  Master via serial comm, Master  Bonsai
Need to check, are USB power lines shared in rotary joint? If so would make serial comm approach between devices tricky.

## Slide 3
On rotary platform
HARP
ONIX Adapter configuration
Required signal transmission
USB camera
2x optical sensor (7 lines) OR 2x USB mouse
2x lick port
2x reward delivery
1x GND
Ephys
Harp configuration
Optical sensor integration x2 (optional with USB mouse)
Lick port signal
Reward signal output
Camera
Adapter USB -- > COAX, communication with ONIX Hub
Rotary joint requirements
2-3 Coax
Pros
No hybrid rotary joints needed, use 2-3Ch high frequency RF coax
Easy to scale up signals leaving the platform, limited by USBcoax bandwidth
More reliable signal transmission through RF coax (vs. USB)
Cons
HARP likely has to be on board rotary platform, hybrid coax USB not readily available
Similarly, camera communication not as trivial as can’t use USB.
Coax rotary joints tend to not have through hole, might require custom development.
Significant development required to develop appropriate Harp  ONIX communication.
If coax through hole rotary joint not available need a different solution for floating treadmill (e.g. bowl ball bearings)
Would need a separate device outside rotary platform to integrate incremental encoder and hall effect sensors
More dependent on custom designs vs. off-the-shelf components
HARP signals must leave platform via USB, can’t interface directly with motor driver (without hybrid rotary joint)
COAX ADAPTER
HARP
Notes: Add clearer diagram for headstage
Extra board off platform for motor encoder
Need to add trigger for camera to all designs – coming from HARP, more detailed electrical schema for all options